## Slide 1: STORAGE OF FRUITS
A M RASHIDA BANU
ASSISTANT PROFESSOR
DEPARTMENT OF BOTANY
HKRH COLLEGE, UTHAMAPALAYAM,
THENI DISTRICT

## Slide 2: STORAGE OF FRUITS
PRESERVATION OF FRUITS
PREVENTS THE DECAY AND DETERIORATION OF FRUITS

## Slide 3
Fruits respire even after harvest
Low temperature slows down the respiration and prolong the storage life of fruits
During storage they need high moisture and humidity nearly 85-95%
Eg mango,banana,lemon,grapes,sapota,papaya,pine apple,jack,pome granate, guava, cheshew nut

## Slide 4: methods
Air cooled storage
Air cooled storage-refrigerated with ice
Wax emulsions coating
Refrigerated storage
Controlled atmospheric storage
Hypobasic storage
Quick freezing

## Slide 5: Air cooled storage
Stored in insulation buildings in the cool night air
Placed in racks in insulation building
Should not be heaped
Sread on rack
Ventilation must
Open in night to allow cool night air
Shut in day time
All kinds of fruits stored

## Slide 6: Air cooled storage- refrigerated with ice
Fruits are stored with ice and salt and cooled with fans in the warmer periods
All kinds of fruits

## Slide 7: Wax emulsions coating
Fruits are coated with wax emulsion
Wax emulsion-melting paraffin wax along with emulsifiers(boiling soft water is slowly added to the molten mixture and stirred well to make a stable emulsion. This wax emulsion is called as C.F.T.R.I wax emulsion(central food technological research institute))
Fruts dipped for a minute in wax emulsion
Dried for 10 -15 mins
Wax should be removed before consumption
Imparts a glossy appearance
Sathukuddi, apple, limes, lemons.

## Slide 8: Refrigerated storage
Fruits stored with the use of refrigerants such as Freon, ammonia methyl chloride and liquid nitrogen.
Most efficient and scientific way
Stored successfully irrespective of the temperature of the external air
Freon – refrigerant which is non-toxic and odourless but ammonia is toxic
Liquid nitrogen is an important refrigerant used for storing fruits like tomatoes, strawberries, apple

## Slide 9: Controlled atmospheric storage(CAS)
Storage of fruits using gases like CO2 and 02
The gases are used in controlled atmospheric storage. In gas storage, the rate of respiration is reduced by
Lowering the temperature
By reducing the 02 supply
By increasing the amount of CO2 around the fruit
Combination of all the three is necessary for storing fruits
Apple can be stored in controlled atmospheric storage with 10%of CO2, 11% OF O2 with a temperature of 4%

## Slide 10: HYPOBASIC STORAGE(HBS)
Storage of fruits using sub-atmospheric pressure is called hypobasic storage
All partial pressure of various gases including water vapour are reduced.it reduces the respiration rate, and synthesis of ethylene
This HBS method is a modified atmospheric storage method

## Slide 11: Quick freezing
Storage of fruits in low temperature is called quick freezing
Storage fruits are treated with low temperature as much as -40o to -50oF
Stored at a temperature of -15of
Low temperature in quick freezing stops all enzyme activity and conserves sugar minerals, vitamin etc

## Slide 12
Name of the fruit | Storage temperature oC | Relative humidity% | Storage life
Mango | 9-10 | 85-90 | 4 WEEKS
Banana | 12.5-14.5 | 85-90 | 3 WEEKS
Grapes | 0-2 | 80-85 | 2-4 WEEKS
Apple | 0-2 | 85-90 | 4-8 MONTHS
Guava | 9-10 | 85-90 | 3 WEEKS
Orange | 6-6.5 | 85-90 | 18 WEEKS