## Slide 1
TITLE OF THE COURSE: BIOCHEMICAL TECHNIQUES TOPIC: CENTRIFUGATION HANDLED BY: RM.LAKSHMANAN ASSOCIATE PROFESSOR & HEAD DEPARTMENT OF MICROBIOLOGY HAJEE KARUTHA ROWTHER HOWDIA COLLEGE(AUTONOMOUS), UTHAMAPALAYAM

## Slide 2: CENTRIFUGATION
Contents
Introduction
Centrifuge-Rotors and types
Fixed angle rotors
Swinging bucket rotors
Vertical rotors
Types of centrifugation
Differential centrifugation
Density gradient centrifugation
Isopycnic centrifugation
Rate zonal centrifugation

## Slide 3
Centrifugation is the technique of separating components where the centrifugal force/ acceleration causes the denser molecules to move towards the periphery while the less dense particles move to the center.
The process of centrifugation relies on the perpendicular force created when a sample is rotated about a fixed point.
The rate of centrifugation is dependent on the size and density of the particles present in the solution.

## Slide 4
A centrifuge is a device used to separate components of a mixture on the basis of their size, density, the viscosity of the medium, and the rotor speed.
The centrifuge is commonly used in laboratories for the separation of biological molecules from a crude extract.
In a centrifuge, the sample is kept in a rotor that is rotated about a fixed point (axis), resulting in strong force perpendicular to the axis.
There are different types of centrifuge used for the separation of different molecules, but they all work on the principle of sedimentation.

## Slide 5
Rotors in centrifuges are the motor devices that house the tubes with the samples. Centrifuge rotors are designed to generate rotation speed that can bring about the separation of components in a sample. There are three main types of rotors used in a centrifuge, which are:
1. Fixed angle rotors
2. Swinging bucket rotors/ Horizontal rotors
3. Vertical rotors

## Slide 6
1.Fixed angle rotors
These rotors hold the sample tubes at an angle of 45° in relation to the axis of the rotor.
In this type of rotor, the particles strike the opposite side of the tube where the particles finally slide down and are collected at the bottom.
These are faster than other types of rotors as the pathlength of the tubes increases.
However, as the direction of the force is different from the position of the tube, some particles might remain at the sides of the tubes.

## Slide 7
2. Swinging bucket rotors/ Horizontal rotors
Swinging bucket rotors hold the tubes at an angle of 90° as the rotor swings as the process is started.
In this rotor, the tubes are suspended in the racks that allow the tubes to be moved enough to acquire the horizontal position.
In this type of rotors, the particles are present along the direction or the path of the force that allows the particles to be moved away from the rotor towards the bottom of the tubes.
Because the tubes remain horizontal, the supernatant remains as a flat surface allowing the deposited particles to be separated from the supernatant.

## Slide 8
3. Vertical rotors
Vertical rotors provide the shortest pathlength, fastest run time, and the highest resolution of all the rotors.
In vertical rotors, the tubes are vertical during the operation of the centrifuge.
The yield of the rotor is not as ideal as the position of the tube doesn’t align with the direction of the centrifugal force.
As a result, instead of settling down, particles tend o spread towards the outer wall of the tubes.
These are commonly used in isopycnic and density gradient centrifugation.

## Slide 9: TYPES OF CENTRIFUGATION
There are two main types of centrifugation.
They are Differential centrifugation and Density gradient centrifugation.
Differential centrifugation
Differential centrifugation is a type of centrifugation process in which components are separately settled down a centrifuge tube by applying a series of increasing centrifugal force.

## Slide 10
Principle of Differential centrifugation
Differential centrifugation is based upon the differences in the sedimentation rate of biological particles of different size and density.
As the increasing centrifugal force is applied, initial sedimentation of the larger molecules takes place.
Further particles settle down depending upon the speed and time of individual centrifugation steps and the density and relative size of the particles.
The largest class of particles forms a pellet on the bottom of the centrifuge tube, leaving smaller-sized structures within the supernatant.
Thus, larger molecules sediment quickly and at lower centrifugal forces whereas the smaller molecules take longer time and higher forces.
In the case of particles that are less dense than the medium, the particles will float instead of settling.

## Slide 11
Steps of Differential centrifugation
The sample solution is homogenized in the medium containing buffer.
The sample is then placed in the centrifuge tube, which is operated at a particular centrifugal force for a specific time at a particular temperature.
By the end of this operation, a pellet will be formed at the bottom of the tube, which is separated from the supernatant.
The supernatant is added to a new centrifuge tube where it is centrifuged at another speed for a particular time and particular temperature.
Again, the supernatant is separated from the pellets formed.
These steps are continued until all particles are separated from each other.
The particles can then be identified by testing for indicators that are unique to the specific particles.

## Slide 12
Uses of Differential centrifugation
Differential centrifugation is commonly used for the separation of cell organelles and membranes found in the cell.
It can also be used for low-resolution separation of the nucleus.
As this technique separates particles based on their sizes, this can be used for the purification of extracts containing larger-sized impurities.

## Slide 13
Density gradient centrifugation
Density gradient centrifugation is the separation of molecules where the separation is based on the density of the molecules as they pass through a density gradient under a centrifugal force.

## Slide 14
Principle of Density gradient centrifugation
Density gradient centrifugation is based on the principle that molecules settle down under a centrifugal force until they reach a medium with the density the same as theirs.
In this case, a medium with a density gradient is employed, which either has to decrease density or increasing density.
Molecules in a sample move through the medium as the sample is rotated creating a centrifugal force.
The more dense molecules begin to move towards the bottom as they move through the density gradient.
The molecules then become suspended at a point in which the density of the particles equals the surrounding medium.
In this way, molecules with different densities are separated at different layers which can then be recovered by various processes.

## Slide 15
Steps of Density gradient centrifugation
A density gradient of a medium is created by gently laying the lower concentration over the higher concentrations in a centrifuge tube.
The sample is then placed over the gradient, and the tubes are placed in an ultracentrifuge.
The particles travel through the gradient until they reach a point at which their density matches the density of the surrounding medium.
The fractions are removed and separated, obtaining the particles as isolated units.

## Slide 16
Uses of Density gradient centrifugation
Density gradient centrifugation can be applied for the purification of large volumes of biomolecules.
It can even be used for the purification of different viruses which aids their further studies.
This technique can be used both as a separation technique and the technique for the determination of densities of various particles.
Density gradient centrifugation is of two types.
They are Isopycnic centrifugation and Rate-zonal density gradient centrifugation

## Slide 17
Isopycnic centrifugation
Isopycnic centrifugation is a type of centrifugation where the particles in a sample are separated on the basis of their densities as centrifugal force is applied to the sample.

## Slide 18
Principle of Isopycnic centrifugation
Isopycnic centrifugation is also termed the equilibrium centrifugation as the separation of particles takes place solely on the basis of their densities and not on their sizes.
The particles move towards the bottom, and the movement is based on the size of the particles. And, the flow ceases once the density of the particle becomes equal to the density of the surrounding medium.
The density in the gradient increases as we move down the tube towards the bottom. As a result, the particles with higher densities settle down at the bottom, followed by less dense particles that form bands above the denser particles.
It is considered as a true equilibrium as this depends directly on the buoyant densities and not the sizes of the particles.

## Slide 19
Steps of Isopycnic centrifugation
A gradient prepared with an increasing density towards the bottom of the tube is prepared. A pre-performed gradient can also be used.
The solution of the biological sample and salt is uniformly distributed in the centrifuge tube and placed inside the centrifuge.
Once the centrifuge is operated, a density gradient of the salt is formed in the tube.
The particles move down the tube and settle down as they reach the region with their respective densities.
The particles are then separated and identified using different other processes.

## Slide 20
Uses of Isopycnic centrifugation
Isopycnic centrifugation can be applied for the purification of large volumes of biomolecules.
This technique can be used as a technique for the determination of densities of various particles.

## Slide 21
Rate-zonal density gradient centrifugation/ Moving Zone Centrifugation
Rate-zonal density gradient centrifugation is a type of centrifugation that separates particles on the basis of their shape as size and works on the same principle of density gradient centrifugation but works in a different way. It is also called the moving zone centrifugation.

## Slide 22
Principle of Rate-zonal density gradient centrifugation
Rate zonal centrifugation fractionates particles by both size and shape.
The procedure is to layer a sample in a restricted zone on top of a pre-poured density gradient. The density gradient is then centrifuged.
All particles migrate into the density gradient because the density gradient has only densities much lower than the densities of the particles being centrifuged.
The particles are fractionated primarily by size and shape. The larger a particle is, the more rapidly it sediments.
The more spherically symmetrical a particle is, the more rapidly it sediments.
The particles sediment through the gradient at a rate that is a function of their sedimentation coefficient.
Unlike differential centrifugation where the sample is distributed throughout the medium, in rate-zonal centrifugation, the sample is initially present only on top of the gradient as a narrow band.

## Slide 23
Steps of Rate-zonal density gradient centrifugation
A density gradient is prepared in a centrifuge tube before applying the sample.
The same is then layered on the top of the gradient in the form of a band.
During centrifugation, fast-moving particles (larger in size and circular in shape) move ahead of slower particles so that different particles are separated as various bands on different parts of the gradient.
The particles are separated on the basis of their sedimentation coefficients, and they are obtained from the bottom of the tube through a perforation.

## Slide 24
Uses of Rate-zonal density gradient centrifugation
Rate-zonal differential centrifugation has been used for the separation of viruses as they have components that are of different size and density that are unique to each virus.
This method has been employed for the fractionation of RNA on sucrose gradients.
Besides, rate-zonal differential centrifugation has also been used for the separation, purification and fractionation of DNA molecules from both viruses and bacteria.
The fractionation of polysomes and ribosome subunits has been one of the earliest applications of this method.