## Slide 1: TITLE OF THE COURSE: BIOCHEMICAL TECHNIQUES TOPIC: ELECTROPHORESIS HANDLED BY: RM.LAKSHMANAN ASSOCIATE PROFESSOR & HEAD DEPARTMENT OF MICROBIOLOGY HAJEE KARUTHA ROWTHER HOWDIA COLLEGE(AUTONOMOUS), UTHAMAPALAYAM

## Slide 2: ELECTROPHORESIS
Contents
Definition
Types of electrophoresis
Agarose gel electrophoresis
Principle
Requirements
Procedure
Applications
SDS-PAGE
Principle
Requirements
Procedure
Applications

## Slide 3
The term electrophoresis describes the migration of a charged particle under the influence of electric field (electro-charged particle and phoresis-movement).
Many important biological molecules such as amino acids, peptides, proteins, nucleotides, nucleic acids possess ionizable groups and, therefore, at any given pH, exists in solution as electrically charged species either as cations or anions.
Under the charge of an electric field these charged particles will migrate either to cathode or to anode, depending on the nature of their net charge

## Slide 4: TYPES OF ELECTROPHORESIS
There are two types of electrophoresis.
Agarose Gel Electrophoresis and SDS-Polyacrylamide Gel Electrophoresis
Agarose Gel Electrophoresis is mainly used for separation of DNA.
SDS-PAGE is mainly used for separation of proteins.

## Slide 5: AGAROSE GEL ELECTROPHORESIS
Agarose gel electrophoresis is a method of gel electrophoresis used in biochemistry, molecular biology, genetics, and clinical chemistry to separate a mixed population of macromolecules such as DNA , RNA or proteins in a matrix of agarose.
Agarose is a natural linear polymer extracted from seaweed that forms a gel matrix by hydrogen-bonding when heated in a buffer and allowed to cool.
They are the most popular medium for the separation of moderate and large-sized nucleic acids and have a wide range of separation.

## Slide 6: Principle
Gel electrophoresis separates DNA fragments by size in a solid support medium such as an agarose gel. Sample (DNA) are pipetted into the sample wells, followed by the application of an electric current at the anodal, negative end which causes the negatively-charged DNA to migrate (electrophorese) towards the bottom (cathodal, positive) end.
The rate of migration is proportional to size: smaller fragments move more quickly, and wind up at the bottom of the gel.
DNA is visualized by including in the gel an intercalating dye, ethidium bromide. DNA fragments take up the dye as they migrate through the gel.
Illumination with ultraviolet light causes the intercalated dye to fluoresce.
The larger fragments fluoresce more intensely.

## Slide 7: Requirements
The equipment and supplies necessary for conducting agarose gel electrophoresis are relatively simple and include:
An electrophoresis chamber and power supply
Gel casting trays, which are available in a variety of sizes and composed of UVtransparent plastic. The open ends of the trays are closed with tape while the gel is being cast, then removed prior to electrophoresis.
Sample combs, around which molten medium is poured to form sample wells in the gel.
Electrophoresis buffer, usually Tris-acetate-EDTA (TAE) or Tris-borate-EDTA (TBE).

## Slide 8
Loading buffer, which contains something dense (e.g. glycerol) to allow the sample to “fall” into the sample wells, and one or two tracking dyes, which migrate in the gel and allow visual monitoring or how far the electrophoresis has proceeded.
Staining: DNA molecules are easily visualized under an ultraviolet lamp when electrphoresed in the presence of the extrinsic fluor ethidium bromide. Alternatively, nucleic acids can be stained after electrophoretic separation by soaking the gel in a solution of ethidium bromide. When intercalated into doublestranded DNA, fluorescence of this molecule increases greatly. It is also possible to detect DNA with the extrinsic fluor 1-anilino 8-naphthalene sulphonate.
Transilluminator (an ultraviolet light box), which is used to visualize stained DNA in gels.

## Slide 9: Procedure
To prepare gel, agarose powder is mixed with electrophoresis buffer to the desired concentration, and heated in a microwave oven to melt it.
The concentration of Agarose Gel
The percentage of agarose used depends on the size of fragments to be resolved.
The concentration of agarose is referred to as a percentage of agarose to volume of buffer (w/v), and agarose gels are normally in the range of 0.2% to 3%.

## Slide 10
Ethidium bromide is added to the gel (final concentration 0.5 ug/ml) to facilitate visualization of DNA after electrophoresis.
After cooling the solution to about 60 degree C, it is poured into a casting tray containing a sample comb and allowed to solidify at room temperature.
After the gel has solidified, the comb is removed, taking care not to rip the bottom of the wells.
The gel, still in plastic tray, is inserted horizontally into the electrophoresis chamber and is covered with buffer.

## Slide 11
Samples containing DNA mixed with loading buffer are then pipetted into the sample wells, the lid and power leads are placed on the apparatus, and a current is applied.
The current flow can be confirmed by observing bubbles coming off the electrodes.
DNA will migrate towards the positive electrode, which is usually colored red, in view of its negative charge.
The distance DNA has migrated in the gel can be judged by visually monitoring migration of the tracking dyes like bromophenol blue and xylene cyanol dyes

## Slide 12: Applications
Agarose gel electrophoresis is a routinely used method for separating DNA or RNA.
Estimation of the size of DNA molecules
Analysis of PCR products, e.g. in molecular genetic diagnosis or genetic fingerprinting
Separation of restricted genomic DNA prior to Southern analysis, or of RNA prior to Northern analysis.
The agarose gel electrophoresis is widely employed to estimate the size of DNA fragments after digesting with restriction enzymes, e.g. in restriction mapping of cloned DNA.
Agarose gel electrophoresis is commonly used to resolve circular DNA with different supercoiling topology, and to resolve fragments that differ due to DNA synthesis.
In addition to providing an excellent medium for fragment size analyses, agarose gels allow purification of DNA fragments.

## Slide 14: SDS-PAGE
Polyacrylamide gel electrophoresis (PAGE) is a technique in biochemistry, forensic chemistry, genetics, molecular biology and biotechnology to separate biological macromolecules, usually proteins , according to their electrophoretic mobility.
The most commonly used form of polyacrylamide gel electrophoresis is the Sodium dodecyl suplhate Polyacrylamide gel electrophoresis (SDS- PAGE) used mostly for the separation of proteins.

## Slide 15
Polyacrylamide gels are chemically cross-linked gels formed by the polymerization of acrylamide with a cross-linking agent, usually N,N’-methylenebisacrylamide.
The reaction is a free radical polymerization, usually carried out with ammonium persulfate as the initiator and N,N,N’,N’-tetramethylethylendiamine (TEMED) as the catalyst.

## Slide 16: Principle
SDS-PAGE (Polyacrylamide Gel Electrophoresis), is an analytical method used to separate components of a protein mixture based on their size.
The technique is based upon the principle that a charged molecule will migrate in an electric field towards an electrode with opposite sign. The general electrophoresis techniques cannot be used to determine the molecular weight of biological molecules because the mobility of a substance in the gel depends on both charge and size

## Slide 17
To overcome this, the biological samples needs to be treated so that they acquire uniform charge, then the electrophoretic mobility depends primarily on size.
For this different protein molecules with different shapes and sizes, needs to be denatured (done with the aid of SDS) so that the proteins lose their secondary, tertiary or quaternary structure .
The proteins being covered by SDS are negatively charged and when loaded onto a gel and placed in an electric field, it will migrate towards the anode (positively charged electrode) are separated by a molecular sieving effect based on size.
After the visualization by a staining (protein-specific) technique, the size of a protein can be calculated by comparing its migration distance with that of a known molecular weight ladder (marker)

## Slide 18: Requirements
Acrylamide solutions (for resolving & stacking gels).
Isopropanol / distilled water.
Gel loading buffer.
Running buffer.
Staining, destaining solutions.
Protein samples
Molecular weight markers.
An electrophoresis chamber and power supply.
Glass plates (a short and a top plate).
Casting frame
Casting stand
Combs

## Slide 19: Procedure
Sample preparation
Samples may be any material containing proteins.
The sample to analyze is optionally mixed with a chemical denaturant if so desired, usually SDS for proteins
SDS is an anionic detergent that denatures secondary and non–disulfide–linked tertiary structures, and additionally applies a negative charge to each protein in proportion to its mass..
A tracking dye may be added to the solution. This typically has a higher electrophoretic mobility than the analytes to allow the experimenter to track the progress of the solution through the gel during the electrophoretic run.

## Slide 20
Preparation of polyacrylamide gel
The gels typically consist of acrylamide, bisacrylamide, the optional denaturant (SDS or urea), and a buffer with an adjusted pH.
The ratio of bisacrylamide to acrylamide can be varied for special purposes, but is generally about 1 part in 35. The acrylamide concentration of the gel can also be varied, generally in the range from 5% to 25%.
Lower percentage gels are better for resolving very high molecular weight molecules, while much higher percentages of acrylamide are needed to resolve smaller proteins,
Gels are usually polymerized between two glass plates in a gel caster, with a comb inserted at the top to create the sample wells.
After the gel is polymerized the comb can be removed and the gel is ready for electrophoresis.

## Slide 21
Electrophoresis
Various buffer systems are used in PAGE depending on the nature of the sample and the experimental objective.
The buffers used at the anode and cathode may be the same or different.
An electric field is applied across the gel, causing the negatively charged proteins or nucleic acids to migrate across the gel away from the negative and towards the positive electrode (the anode).

## Slide 22
Depending on their size, each biomolecule moves differently through the gel matrix: small molecules more easily fit through the pores in the gel, while larger ones have more difficulty.
The gel is run usually for a few hours, though this depends on the voltage applied across the gel.
After the set amount of time, the biomolecules will have migrated different distances based on their size.
Smaller biomolecules travel farther down the gel, while larger ones remain closer to the point of origin.

## Slide 23
Detection
Following electrophoresis, the gel may be stained (for proteins, most commonly with Coomassie Brilliant Blue or autoradiography; for nucleic acids, ethidium bromide; or for either, silver stain), allowing visualization of the separated proteins, or processed further (e.g. Western blot).
After staining, different species biomolecules appear as distinct bands within the gel.

## Slide 24: Applications
Peptide mapping.
Estimation of protein size.
Determination of protein subunits or aggregation structures.
Estimation of protein purity.
Protein quantitation.
Monitoring protein integrity.