## Slide 1: BIO DIESEL
Dr. A. MAAJITHA BEGAM
ASSISTANT PROFESSOR OF BOTANY
HAJEE KARUTHA ROWTHER HOWDIA COLLEGE
UTHAMAPALAYAM
THENI DISTRICT
TAMILNADU

## Slide 2: Biodiesel - Introduction
Biodiesel is a clean burning oil manufactured from fat or vegetable oils by transesterification process.
It is not petroleum origin
It is biodegradable
Non-toxic
Free from sulphur and aromatics
Used with no or little modification

## Slide 3
Fuel engines designed till 1993 could not use 100 % biodiesel because they had rubber seals
Modern engines does not have the rubber seal so that 100% biodiesel can be used
It is used to run vehicles, generators, boats and so on.
Biodiesel can be produces from algae and many plants

## Slide 4: Jatropha
Bio fuel is prepared from plant oils. It is known as biodiesel.
Jatropha curcus
Euphorbiaceae
3 to 5cm in height
Lobed leaves with spiral phyllotaxy
Fruits produced after a year of plantation
Plant can grow anywhere.

## Slide 5
Production of Bio diesel involves the following steps
    Preparation of Jatropha Seeds
    Extraction of Oils
    Purification of Oils
    Transesterification

## Slide 6: jatropha CURCUS

## Slide 7: Preparation of seeds and extraction
Plucking of ripened fruits
Decorticated
sundried

## Slide 8
Mechanical Extraction by screw press / Solvent extraction/ Sox-let extraction
Removal of suspended particles by filtration
Boiled with 20% of water
Decantation
Boiling
Decantation

## Slide 9: transesterification
NaOH/KOH mixed with methanol
Dissolve hydroxide
Sodium methoxide/Potassium methoxide
Sodium methoxide mixture is added to hot Jatropha Oil
Mixed well for 10 mins

## Slide 10: Transesterfication
Methanol reacts with the fatty acids of the jatropha oil to produce mono alkyl ester (biodiesel) and glycerol.
Transesterification - One alcohol is displaced from an ester by another alcohol
Allowed to sediment for 8 -24 hrs
Glycerol settled at bottom and it is drained off
NaOH & KOH acted as Catalyst

## Slide 11
Sodium hydroxide + Methanol Sodium methoxide
Sodium methoxide + Jatropha Oil Mono alkyl ester (Biodiesel) + Glycerol
Jatropha Oil + Methanol + NaOH Glycerol + BIodiesel
Overall process

## Slide 14
THANKS