## Slide 1: Network Topologies
CLASS: I M.COM CA
PG DEPARTMENT OF COMMERCE CA
STAFF NAME: R.ABIRAMAKRISHNAN.

## Slide 2: Objectives
Describe the basic and hybrid LAN physical topologies, and their uses, advantages and disadvantages
Describe the backbone structures that form the foundation for most LANs

## Slide 3: Simple Physical Topologies
Physical topology: physical layout of nodes on a network
Three fundamental shapes:
  Bus
  Ring
  Star
May create hybrid topologies
Topology integral to type of network, cabling infrastructure, and transmission media used

## Slide 4: Bus
Single cable connects all network nodes without intervening connectivity devices
Devices share responsibility for getting data from one point to another
Terminators stop signals after reaching end of wire
  Prevent signal bounce
Inexpensive, not very scalable
Difficult to troubleshoot, not fault-tolerant

## Slide 5: Bus (continued)

## Slide 6: Advantages & Disadvantages of Bus Topology
Advantages
Works well for small networks
Relatively inexpensive to implement
Easy to add to it
Disadvantages
Management costs can be high
Potential for congestion with network traffic

## Slide 7: Ring

## Slide 8: Simple Physical Topologies
Ring topology
  Each node is connected to the two nearest nodes so the entire network forms a circle
  One method for passing data on ring networks is token passing
Active topology
  Each workstation transmits data

## Slide 9: Advantages of Ring Topology
Easier to manage; easier to locate a defective node or cable problem
Well-suited for transmitting signals over long distances on a LAN
Handles high-volume network traffic
Enables reliable communication

## Slide 10: Disadvantages of Ring Topology
Expensive
Requires more cable and network equipment at the start
Not used as widely as bus topology
  Fewer equipment options
  Fewer options for expansion to high-speed communication

## Slide 11: Star

## Slide 12: Simple Physical Topologies
Star topology
  Every node on the network is connected through a central device

## Slide 13: Star (continued)
Any single cable connects only two devices
  Cabling problems affect two nodes at most
Requires more cabling than ring or bus networks
  More fault-tolerant
Easily moved, isolated, or interconnected with other networks
  Scalable
Supports max of 1024 addressable nodes on logical network

## Slide 14: Advantages & Disadvantages of Star Topology
Advantages
Good option for modern networks
Low startup costs
Easy to manage
Offers opportunities for expansion
Most popular topology in use; wide variety of equipment available
Disadvantages
Hub is a single point of failure
Requires more cable than the bus

## Slide 15: Hybrid Physical Topologies: Star-Wired Ring

## Slide 16: Star-Wired Bus

## Slide 17: Backbone Networks: Serial Backbone
Daisy chain: linked series of devices
  Hubs and switches often connected in daisy chain to extend a network
Hubs, gateways, routers, switches, and bridges can form part of backbone
Extent to which hubs can be connected is limited

## Slide 18: Logical Topologies
Logical topology: how data is transmitted between nodes
  May not match physical topology
Bus logical topology: signals travel from one network device to all other devices on network
  Required by bus, star, star-wired physical topologies
Ring logical topology: signals follow circular path between sender and receiver
  Required by ring, star-wired ring topologies