## Slide 1: LAPLACE TRANSFORMS
SOLUTION PROCESS
Presented by
Dr.S.Mohamed Basheer
Assistant professor
Department of Mathematics

## Slide 2: Solution process (1 of 8)
Any nonhomogeneous linear differential equation with constant coefficients can be solved with the following procedure, which reduces the solution to algebra
4. Laplace transforms

## Slide 3: Solution process (2 of 8)
Step 1: Put differential equation into standard form
  D2 y + 2D y + 2y = cos t
  y(0) = 1
  D y(0) = 0

## Slide 4: Solution process (3 of 8)
Step 2: Take the Laplace transform of both sides
  L{D2 y} + L{2D y} + L{2y} = L{cos t}

## Slide 5: Solution process (4 of 8)
Step 3: Use table of transforms to express equation in s-domain
  L{D2 y} + L{2D y} + L{2y} = L{cos  t}
  L{D2 y} = s2 Y(s) - sy(0) - D y(0)
  L{2D y} = 2[ s Y(s) - y(0)]
  L{2y} = 2 Y(s)
  L{cos t} = s/(s2 + 1)
  s2 Y(s) - s + 2s Y(s) - 2 + 2 Y(s) = s /(s2 + 1)

## Slide 6: Solution process (5 of 8)
Step 4: Solve for Y(s)
  s2 Y(s) - s + 2s Y(s) - 2 + 2 Y(s) = s/(s2 + 1)
  (s2 + 2s + 2) Y(s) = s/(s2 + 1) + s + 2
  Y(s) = [s/(s2 + 1) + s + 2]/ (s2 + 2s + 2)
  = (s3 + 2 s2 + 2s + 2)/[(s2 + 1) (s2 + 2s + 2)]

## Slide 7: Solution process (6 of 8)
Step 5: Expand equation into format covered by table
  Y(s) = (s3 + 2 s2 + 2s + 2)/[(s2 + 1) (s2 + 2s + 2)]
  = (As + B)/ (s2 + 1) + (Cs + E)/ (s2 + 2s + 2)
  (A+C)s3 + (2A + B + E) s2 + (2A + 2B + C)s + (2B +E)
  1 = A + C
  2 = 2A + B + E
  2 = 2A + 2B + C
  2 = 2B + E
  A = 0.2, B = 0.4, C = 0.8, E = 1.2

## Slide 8: Solution process (7 of 8)
  (0.2s + 0.4)/ (s2 + 1)
  = 0.2 s/ (s2 + 1) + 0.4 / (s2 + 1)
  (0.8s + 1.2)/ (s2 + 2s + 2)
  = 0.8 (s+1)/[(s+1)2 + 1] + 0.4/ [(s+1)2 + 1]

## Slide 9: Solution process (8 of 8)
Step 6: Use table to convert s-domain to time domain
  0.2 s/ (s2 + 1) becomes 0.2 cos t
  0.4 / (s2 + 1) becomes 0.4 sin t
  0.8 (s+1)/[(s+1)2 + 1] becomes 0.8 e-t cos t
  0.4/ [(s+1)2 + 1] becomes 0.4 e-t sin t
  y(t) = 0.2 cos t + 0.4 sin t + 0.8 e-t cos t + 0.4 e-t sin t

## Slide 10: LAPLACE TRANSFORMS
TRANSFER FUNCTIONS

## Slide 11: Introduction
Definition -- a transfer function is an expression that relates the output to the input in the s-domain
differential
equation
r(t)
y(t)
transfer
function
r(s)
y(s)
5. Transfer functions

## Slide 12: Transfer Function
Definition
  H(s) = Y(s) / X(s)
Relates the output of a linear system (or component) to its input
Describes how a linear system responds to an impulse
All linear operations allowed
  Scaling, addition, multiplication
H(s)
X(s)
Y(s)

## Slide 13: Block Diagrams
Pictorially expresses flows and relationships between elements in system
Blocks may recursively be systems
Rules
  Cascaded (non-loading) elements: convolution
  Summation and difference elements
Can simplify

## Slide 14: Typical block diagram
control
Gc(s)
plant
Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
reference input, R(s)
error, E(s)
plant inputs, U(s)
output, Y(s)
feedback, H(s)Y(s)
5. Transfer functions

## Slide 15: Example
v(t)
R
C
L
v(t) = R I(t) + 1/C I(t) dt + L di(t)/dt
V(s) = [R I(s) + 1/(C s) I(s) + s L I(s)]
Note: Ignore initial conditions
5. Transfer functions

## Slide 16: Block diagram and transfer function
V(s)
  = (R + 1/(C s) + s L ) I(s)
  = (C L s2 + C R s + 1 )/(C s) I(s)
I(s)/V(s) = C s / (C L s2 + C R s + 1 )
C s / (C L s2 + C R s + 1 )
V(s)
I(s)
5. Transfer functions

## Slide 17: Block diagram reduction rules
G1
G2
G1 G2
U
Y
U
Y
G1
G2
U
Y
+
+
G1 + G2
U
Y
G1
G2
U
Y
+
-
G1 /(1+G1 G2)
U
Y
Series
Parallel
Feedback
5. Transfer functions

## Slide 18: Rational Laplace Transforms
Notes: Jlh: Need to give insights into why poles and zeroes are important. Otherwise, the audience will be overwhelmed.

## Slide 19: First Order System
Reference
S
1
Notes: Examples of transducers in computer systems are mainly surrogate variables. For example, we may not be able to measure end-user response times. However, we can measure internal system queueing. So we use the latter as a surrogate for the former and sometimes use simple equations (e.g., Little’s result) to convert between the two.
Use the approximation to simplify the following analysis
Another aspect of the transducer are the delays it introduces. Typically, measurements are sampled. The sample rate cannot be too fast if the performance of the plant (e.g., database server) is

## Slide 20: First Order System
Impulse response |  | Exponential
Step response |  | Step, exponential
Ramp response |  | Ramp, step, exponential
No oscillations (as seen by poles)
Notes: Jlh: Haven’t explained the relationship between poles and oscillations

## Slide 21: Second Order System
Notes: Get oscillatory response if have poles that have non-zero Im values.

## Slide 22: Second Order System: Parameters
Notes: Get oscillatory response if have poles that have non-zero Im values.

## Slide 23: Transient Response Characteristics

## Slide 24: Transient Response
Estimates the shape of the curve based on the foregoing points on the x and y axis
Typically applied to the following inputs
  Impulse
  Step
  Ramp
  Quadratic (Parabola)

## Slide 25: Effect of pole locations
Faster Decay
Faster Blowup
Oscillations
(higher-freq)
Im(s)
Re(s)
(e-at)
(eat)

## Slide 26: Basic Control Actions: u(t)
Notes: Jlh: Can we give more intuition on control actions. This seems real brief considering its importance.

## Slide 27: Effect of Control Actions
Proportional Action
  Adjustable gain (amplifier)
Integral Action
  Eliminates bias (steady-state error)
  Can cause oscillations
Derivative Action (“rate control”)
  Effective in transient periods
  Provides faster response (higher sensitivity)
  Never used alone

## Slide 28: Basic Controllers
Proportional control is often used by itself
Integral and differential control are typically used in combination with at least proportional control
  eg, Proportional Integral (PI) controller:

## Slide 29: Summary of Basic Control
Proportional control
  Multiply e(t) by a constant
PI control
  Multiply e(t) and its integral by separate constants
  Avoids bias for step
PD control
  Multiply e(t) and its derivative by separate constants
  Adjust more rapidly to changes
PID control
  Multiply e(t), its derivative and its integral by separate constants
  Reduce bias and react quickly

## Slide 30: Root-locus Analysis
Based on characteristic eqn of closed-loop transfer function
Plot location of roots of this eqn
  Same as poles of closed-loop transfer function
  Parameter (gain) varied from 0 to 
Multiple parameters are ok
  Vary one-by-one
  Plot a root “contour” (usually for 2-3 params)
Quickly get approximate results
  Range of parameters that gives desired response