## Slide 1
Raw materials of Fermentation
Product
Prepared by
Dr. P. Sivamanikandan
Assistant Professor of Microbiology
Hajee Karutha Rowther Howdia College(Autonomous),
Uthamapalayam-625533

## Slide 2
Introduction
All micro-organisms require water, sources of energy, carbon, nitrogen, mineral elements and possibly vitamins and oxygen if aerobic.
The use of cane molasses, beet molasses, cereal grains, starch, glucose, sucrose and lactose as carbon sources, and ammonium salts, urea, nitrates, corn steep liquor, Soya bean meal, slaughter-house waste and fermentation residues as nitrogen sources, for the production media.
Many different types of raw material are used in different types of industrial fermentation processes.
Mostly agricultural products are utilized as sources of raw material in fermentation industries.

## Slide 3
The main features that involve the raw materials are as follows.
Cost and availability: ideally, raw materials should be low-cost and constant quality.
Easy of handling in solid or liquid forms, along with associated transport and storage
These wastes contain a large amount of proteins and carbohydrates.
The concentration of target product reached its rate of formation and yield per gram of substrate utilized.
Overall health and safety implications.

## Slide 4
Carbon sources
Carbon sources are the major components of media. It is building blocks for growth and product formation.
The carbon sources give fast growth and depress the formation of some products.
A carbon source is required for all biosynthesis important to reproduction, product formation and cell maintenance.
As most carbon substrates also serve as energy sources, the organism’s efficiency of both adenosine triphosphate (ATP) generation.
Animal fats and plant oils may also be included into some media, often as increase to the main carbon source.
Carbohydrates are the energy sources for microbial fermentations, may be used as alcohols, alkanes and organic acids.

## Slide 5
For commercial fermentations the determination of yield coefficients for all other nutrients is usually essential.
For example, Saccharomyces cerevisiae grown on glucose has biomass yield coefficients of 0.56 and 0.12 g under aerobic and anaerobic conditions, respectively.
Molasses
Pure glucose and sucrose are rarely used for industrial scale fermentations, primarily due to cost.
Molasses is a byproduct of the cane and beet sugar production. It is recovered at several stages in the sugar refining industry.
It is dark coloured thick syrup containing 50–60% (w/v) carbohydrates, primarily sucrose, with 2% (w/v) nitrogenous substances, along with some vitamins and minerals.

## Slide 6
Cane Molasses
Cane molasses is rich in vitamin such as biotin, Pantothenic acid, thiamine, phosphorous and sulphur also present.
It is a cheaper and more natural source of sucrose. The chemical composition of sugar cane molasses is water 20%, Ash 8%, Total sugar 40 -60%, Total nitrogen bodies 3%, Total nitrogen 0.5%, gums 2%, free acids 2%, combined acids 3%.
About 95% of the total sugar in cane molasses is fermentable.
The organic nitrogen content is less than beet molasses. It dose not contain betaine.

## Slide 7
Beet molasses
Beet molasses are produced by the same processes employed for cane molasses.
Beet molasses is rich in vitamin such as biotin, pyridoxine, Pantothenic acid, thiamine and inositol, are also present.
It is a cheaper and more natural source of sucrose. The chemical composition of beet molasses is Sucrose 48 -50%, Raffinose 1%, Glucose + fructose 1%, Nitrogen compounds 12 -13%, glutamic acid 3 -5%, Betaine 3.25 – 4.25%, Ash 11- 12%.
The largest utilization of cane molasses in India at present used in the alcohol industry for the manufacture of ethyl alcohol (sprit) and other liquor such as rum, brandy, gin and whiskey.

## Slide 8
Malt Extract
Aqueous extracts of malted barley can be concentrated to form syrups that are particularly useful carbon sources for the cultivation of filamentous fungi, yeasts and Actinomycetes.
The composition of malt extracts varies to 90% carbohydrate including 20% hexoses, 55% disaccharides and 10% maltotriose, a trisaccharide and also contains some vitamins and nitrogenous substances, proteins, peptides and amino acids.

## Slide 9
Whey
Whey is an aqueous byproduct of the dairy industry.
They straw coloured liquid produced as a byproduct of cheese industry.
It is a main waste product for the cheese industry.
It cannot be disposed of without proper treatment.
This material is expensive to store and transport. Therefore, lactose concentrates are prepared for later fermentation by evaporation of the whey, following removal of milk proteins for use as food supplements.
This disaccharide was formerly used in penicillin fermentations and it is still employed for producing ethanol, single cell protein, lactic acid, vitamin B12 and gibberellic acid.

## Slide 10
Sulfite Waste Liquor
In the manufacture of paper pulp, wood is subjected to hydrolysis is brought about with help of calcium bisulfite under heat and pressure. At the end of this process, the spent liquid is formed. This liquid is called Sulfite Waste Liquor.
Waste liquors from coniferous trees contain 2–3% (w/v) sugar, which is a mixture of hexoses (80%) and pentoses (20%). Hexoses include glucose, mannose and galactose, whereas the pentose sugars are mostly xylose and arabinose.
Sugar containing wastes derived from the paper pulping industry are primarily used for the cultivation of yeasts.
Sulfite Waste Liquor obtained from the paper pulp industry cannot be used directly in the fermentations industry. It is essential to remove the free sulfite dioxide present in the waste liquor, since these compounds are toxic to microorganisms.

## Slide 11
Nitrogen sources
Most industrial microbes can utilize both inorganic and organic nitrogen sources.
Inorganic nitrogen may be supplied as ammonium salts, ammonium sulphate and di ammonium hydrogen phosphate, or ammonia.
Ammonia can also be used to adjust the pH of the fermentation. Organic nitrogen sources include amino acids, proteins and urea.
Nitrogen is often supplied in crude forms that are essentially byproducts of other industries, such as corn steep liquor, yeast extracts, peptones and soya meal.

## Slide 12
Corn Steep Liquor
Corn steep liquor is a byproduct of starch extraction from maize and its first use in fermentations was for penicillin production in the 1940s.
The used steep water results from the steeping of corn during the manufacture of starch and other corn products.
The exact composition of the liquor varies depending on the quality of the maize and the processing conditions.
Concentrated extracts generally contain about 4% (w/v) nitrogen, including a wide range of amino acids, along with vitamins and minerals.
Corn steep liquor can be replaced by similar liquors, from potato starch production.

## Slide 13
Soya Bean Meal
Soya bean meal is more complex nitrogenous source then corn steep liquor.
soya beans have been processed to extract the bulk of their oil are composed of 50% protein, 8% non-protein nitrogenous compounds, 30% carbohydrates and 1% oil.
This residual soya meal is used in antibiotic fermentations because the components are only slowly metabolized, thereby eliminating the possibility of repression of product formation.

## Slide 14
ANY
QUESTION

## Slide 15
Thank you
Dr. P. Sivamanikandan
Assistant Professor of Microbiology
Hajee Karutha Rowther Howdia College(Autonomous),
Uthamapalayam-625533